## Slide 1
Project
1. Proposal. Describe the problem you propose to analyze. Include
Background: describe the problem you intend to analyze, give motivation for doing the analysis, cite literature.
Objective: Describe what you intend to achieve as a result of doing the simulation
Method: Describe the analysis you will conduct. This should include a description of the mathematical problem, including governing equation, boundary and initial conditions, parameters, and geometry.
  Verification: Describe existing analyses you would use to verify your results. This could be an analytical solution or existing numerical solution.
  Validation or calibration: Describe data that you would use to calibrate your simulation. Identify the approach you would use for calibration.
  Approach: Outline 3-5 analyses of increasing complexity that ends with the final goal.
Results: Describe the results you expect to get from the analyses.
References: Identify and cite at least 3 papers

## Slide 2: Transport with Fluid-Solid Reactions
Gas chromatograph
http://www.insilico.hu/liesegang/index.html
Ion exchange resin
Mineralized vein

## Slide 3: Reaction Locations
Bulk Material (homogeneous rxn)
Fluid—Multi-scale mixing
Solid– Diffusion dominant
Interfaces (heterogeneous rxn)
Fluid-Solid—No flow at interfacediffusion
Liquid-Gas

## Slide 4: Conceptual Model
Cf
Cs
fluid
solid

## Slide 5: Concentrations
In water:
In soil:
On surfaces:

## Slide 6: Processes
Sorption: bonding, but similar species as aqueous
Precipitation: change species
Clogging: significant thickness
Dissolution: remove solid
Biofilm: growth of filmreactions, clogging
Matrix diffusion: species into matrix, store/react

## Slide 7: Reaction Rates
Fast relative to transport
  Equilibrium
  Partitioning between fluid/solid
  Cs = f(Cf)
Similar or slower than transport
  Disequilibrium, kinetics important
  Reaction time scale: 1/k1
  Diffusion time scale: L2/D
  Advection time scale: L/v

## Slide 8: Sorption Isotherms
https://www.soils.org/publications/sssaj/articles/67/4/1140

## Slide 9: Equilibrium Sorption
Non- linear Isotherm
High concentrations
Examples
Concentration sorbed (mass/mass)
Concentration in water
Concentration sorbed (mass/mass)
Concentration in water
Slope = Distribution Coefficient, Kd
Good for low concentrations
Linear Isotherm
Sorption sites fill at high concentrations

## Slide 10: Important Concept, FluidSolid Surface Porous media, Two overlapping domains
Equilibrium Partitioning
Fluid concentration, Cf[Ms/Lf3]
Solid surface concentration, Cs[Ms/Mso]
Fluid conc
Solid conc

## Slide 11
Effects of Equilibrium Sorption on Transport of a Plume
Source as mass flux over a circular area
Breakthrough curves
Chromatographic eff

## Slide 12: Application of pulse test to determine ne and R
Average linear flow velocity
v=L/tm,w
tm=9215 s (from first moment, conservative tracer)
L=300m (from set up)
v=300m/9215 s =0.032 m/s
Effective porosity
Flux = q =0.01 m/s (specified in model)
Effective porosity =q/v = 0.01/0.032 = 0.31
Compare to porosity specified in model=0.3
Retardation factor
vc=L/tm,c
tm=20700 s (from first moment sorbing compound)
v=300m/20700 s =0.014 m/s
L
R=vw/vc= 0.032/0.014=2.3
Chromatographic effect

## Slide 13
Rate of change due to sorption

## Slide 14
Storage
Advective Flux
Diffusive Flux (Fick’s Law)
Dispersive Flux
Source
Governing
Governing Equation
Advection-Dispersion w/ surface reaction
c = Cn

## Slide 15: Governing Eq. AD w/Equilibrium Sorption, Linear Isotherm
Linear Isotherm
Retardation factor

## Slide 16: Governing Eq. AD w/Equilibrium Sorption, Langmuir Isotherm
Langmuir Isotherm
Retardation factor

## Slide 17: Governing Eq. AD w/Equilibrium Sorption, Linear Isotherm Comsol format
Linear Isotherm
Retardation factor
For Reference

## Slide 18: Nonequilibrium (Kinetic) Sorption Macroscopic, Two adjacent domains
Fluid concentration, Cf ,[mol/m3]
Solid surface concentration, Cs , [mol/m2]
kads: sorption rate constant [1/(m s)]
kdes: desorption rate constant [1/s]
Transport bulk fluid solid = Solid rxn rate
Cf
Cf
Cs
Cs
Jboundary
1st order sorption kinetics
reversible
Mass flux boundary condition
on fluid
Fluid
solid

## Slide 19: Nonequilibrium Sorption Kinetics
http://www.sciencedirect.com/science/article/pii/S0883292706002629#

## Slide 20
Cf
Cs
Fluid
solid
Non-equilibrium Sorption
Pore-scale
Specify rate of change of Cs
First-order irreversible kinetics
First-order reversible
Solid Fluid

## Slide 21: Important Concept, FluidSolid Surface Porous media, Two overlapping domains
Dual Porosity, Dual Permeability
Two domains
(fractures, matrix)
(fluid, solid)
(liquid, gas)
Usually contrasting k
Mass transfer between domains

## Slide 22
Example
First-order non-equilib sorption
Reversible and irreversible
water
solid
Non-reversible
water
reversible
Cwater
Left behind on solid
Breakthrough curves

## Slide 23
Governing Equation
Advection-Dispersion w/ surface reaction
Dual Porosity Approach, with concentrations in both domains
Advection
Diffusion only

## Slide 24
Clogging of a flow channel from precipitation on wall
Non-equilibrium sorption
Pipes clogged with precipitate
Plaque clogging artery
Biofilm
Cementation of pore space
biofilm

## Slide 25: Biofilm Conceptual Model
Growth/decay of biomass
uptake of nutrients, increase in thickness
decay, decrease in thickness
3D geometry on surface
interaction with flow
fluid sheardetachment
Mass transfer to biofilm
transport through fluid
mass transfer through stagnant water layer
mass transfer within biofilm
Reactions within biofilm
first-order, monod, growth/death other
vary within biofilm
http://www.bti.umn.edu/bond/bond_lab___university_of_minnesota.html
http://wyss.harvard.edu/viewmedia/133/bacterial-biofilm-1;jsessionid=6F46332D65A9586919824B047248B4E0.wyss2

## Slide 26: Clogging and Channeling
Fluid concentration, Cf ,[mol/m3]
Solid surface concentration, Cs , [mol/m2]
Solid concentration, Cs , [Ms/Mos]
Macroscopic model
REV Model
Cf
Cs
Fluid
solid
[]velocity of interface (moving mesh).
Use to calc rate of change in porosity
Use porosity change to get k change

## Slide 27: Clogging of flow channel from precipitation Non-equilibrium sorption
Cf: fluid concentration [mol/m3]
Cs: concentration on solid [mol/m2]
kads: sorption rate constant [m/s]
kerode: erosion rate constant[mol/m2]
tw: wall shear rate[1/s]
tw: critical wall shear stress for erosion[1/s]
w: thickness of layer along wall [m]
Mvol: Molar volume [m3/mol]
Cf
Cf
Cs
Cs
Jboundary
Fluid
solid
w
w
Reaction
Flux out of fluid
Movement of wall

## Slide 28
0.001m/s P=0
No flow
No flow
Cf=1 Outflow
No diffusive flux
No flux
Flux out = -rxn
Fluid
Transport
In water
Surface reaction
Physics
Laminar flow
  Viscosity = f(C_m)
Transport, rxn
  C_substrate
  C_microbe population
Geometry (mm)
non-reactive | reactive
Example

## Slide 29
https://vimeo.com/65554224
https://vimeo.com/65554293
https://vimeo.com/65554294
Baseline, fluid shear has no effect
Less sensitive to shear
More sensitive to shear
Biofilm growth and clogging

## Slide 31: Strategy
Geometry, definitions, physics
Flow
Flow+transport
Flow+transport+surface rxn
Flow+transport+surface rxn+deformed mesh

## Slide 32
non-reactive | reactive
concentration

## Slide 34
http://ac.els-cdn.com/S0008622304002155/1-s2.0-S0008622304002155-main.pdf?_tid=2c787188-8be7-11e2-b17d-00000aab0f02&acdnat=1363183759_8cfe4ddd81d00a9db89666573888753f