## Slide 1: Heat Transport
Temperature of a wolf pup

## Slide 2
Schlieren image of natural convection. Note laminar-turbulent transition
Goblet filled with coffee and ice water
Thermal plume, Lake Michigan
http://www.geog.ucsb.edu/~jeff/115a/remote_sensing/thermal/thermalirinfo.html
Radiating steel bar
Temperature distribution
Solar radiation
Multiphase flow

## Slide 3: Concepts
Storage
Source
Flux

## Slide 4: Heat Storage
Internal
Energy
[E/M];
[J/kg]
Temperature
solid liquid vapor
Latent heat of fusion
Latent heat of vaporization
Sensible heat

## Slide 5: Heat Storage as Sensible Heat
cp=specific heat capacity = Energy/(Mass Temp)
Change of sensible heat
On a per volume basis
Cpr=Energy/(Vol Temp)
Internal
Energy
(J/kg)
Temperature
Sensible heat

## Slide 6: Specific Heat Capacity
kJ/(kg K)
Water: 4.18
Ice: 2.11
Air: 1.00
CO2: 0.84
Gold: 0.13
Hydrogen: 14 (max)
Span factor of 100
Water in upper 90%

## Slide 7: Heat Storage as Latent Heat
Melting water: 334 kJ/kg
Heating, 0-100oC: 420 kJ/kg
Vaporing water: 2260 kJ/kg
Internal
Energy
(J/kg)
Temperature
solid liquid vapor
Water

## Slide 8: Heat Sources
Friction: fluids, solids, energy dissipation
Chemical reaction: Exo, Endothermic
Radioactive: Fission, fusion
Biological: Metabolism
Dielectric: Microwaves, oven
Joule: Electrical resistance, toaster
Heat generated internally

## Slide 9: Types of heat transfer
Conduction: Static media, Diffusion
Convection: Fluid moving, advection
Forced; Free or Natural
Radiation: Emit and adsorb EM, no media
Thermal flux

## Slide 10: Radiation
T1 T2
s = Stefan-Boltzman constant
5.67x10-8 W/(m2 K4)
= emissivity (0-1); ~1: black; ~0: shiny
Heat transfer flux by radiation
“Black” body absorbs all incoming radiation and is a perfect emitter.
Stefan’s Law
http://www.thermoworks.com/emissivity_table.html

## Slide 11: Thermal Conduction
Fourier’s Law, energy flux
Thermal conductivity

## Slide 12: Thermal conductivity
http://web.mit.edu/lienhard/www/ahttv202.pdf
W/(moC)
Vacuum: 0.001
Air: 0.02
Water: 0.6
Ice: 2
Steel: 10
Copper: 400
Diamond: 1000

## Slide 13: Convection
Forced: Fluid flow driven by processes other than thermal, pump etc.
Free or Natural: Fluid flow by thermally induced density differences
Energy flux:

## Slide 14: Convection
Forced: Fluid flow driven by processes other than thermal, pump etc.
Free or Natural: Fluid flow by thermally induced density differences
Energy flux:

## Slide 15
Convective heat transfer —fluidsolid
Tf
Ts
b

## Slide 16: Convective Heat Transfer Coefficient
http://web.mit.edu/lienhard/www/ahttv202.pdf

## Slide 17
https://docs.google.com/viewer?url=http%3A%2F%2Fwww.bakker.org%2Fdartmouth06%2Fengs150%2F13-heat.pdf

## Slide 18
Storage
Advective Flux
Diffusive Flux (Fick’s Law)
Dispersive Flux
Source
Governing
Governing Equation
Conservation of Heat Energy
c =cprnT
S = Sh

## Slide 19: Simulation of Heat Transport

## Slide 20
Parameters
cp heat capacity
r density
Kh thermal conductivity
q fluid flux
n porosity
Dhyd hydraulic dispersion

## Slide 21: Coupled effects
Chemical reaction rate
Phase change
Material properties
Thermal expansion
Solid-Fluid in porous media
Biological growth

## Slide 22: Temperature and Chemical Rxn
Reaction Rate Constant Function
Arrhenius eq
EA: activation energy for reaction
R: gas constant
T: temperature
A: Max rate term

## Slide 23: Including phase change
Internal
Energy
(J/m3)
Temperature
solid liquid vapor
Cp(E/(kg3q))
Temperature (q)
Area under curve = latent heat

## Slide 24: Fluid properties
Cp(E/(kg3q))
Temperature (q)
Viscosity
Density
Thermal Conductivity

## Slide 25: Thermal expansion
Volumetric
Linear

## Slide 26
Solid Phase in Porous Media
Heat loss by fluid Heat balance between fluid and solid
Tf Ts

## Slide 28: Material Properties
https://docs.google.com/viewer?url=http%3A%2F%2Fwww.bakker.org%2Fdartmouth06%2Fengs150%2F13-heat.pdf

## Slide 29: Heat Transfer by Radiation and Convection

## Slide 31: Conceptual Model
Radiation and convection
Radiation and convection

## Slide 34: U-tube Heat Exchanger
Installation of a U-tube in a borehole
Two pipes from a U-tube heat exchanger in a borehole
U-tube heat exchanger
Array of U-tube heat exchangers

## Slide 36: Free Convection Rayleigh-Bernard Convection Cells

## Slide 37: Convection in the Earth and Atm

## Slide 38: Experiment cooling at the top
http://www.sciencedirect.com/science/article/pii/S0894177707001409
Simulated lake

## Slide 39: Rayleigh number
Onset of natural convection depends on Ra
For a layer with a free top surface: Racrit=1100

## Slide 40: Coefficient of Thermal Expansion

## Slide 41: Effect of varying temperature on mixing in surface water