## Slide 1: Multi-phase flow
Mixture of
  Gas, liquid, solid
  Multiple liquids w/ different properties
Conceptual
  Discrete phases
  Distinct properties, interface
  Mixture
  Properties depend on ratio of phases in mixture

## Slide 2: Important
Surface tension, s
Velocity, v
Size, L
Viscosity, m
Density, r
Dimensionless numbers balancing forces

## Slide 3: Types of flow
Particles in fluid
  Bubbly, sediment, droplets, dust, ash
  Bulk fluid properties vary with concentration
Free surface
  Liquid and gas
  Interface important, ignore properties of one fluid
Multiple fluids
  Slug flow, immiscible liquids, composition contrasts
  Properties of both fluids and interface important
Porous media
  Partly saturated w/ water, multiple fluids
  Properties vary with saturation

## Slide 4: Simulation Methods
Many small discrete particles in fluid
  Vol fraction controls visc/density of mixture,
  Momentum transfer between solid and gas
  Mixture model, Euler-Euler method 1 continuous, 1 dispersed phase
  Particle tracking
Free surface
One fluid with moving interface
  Moving mesh, Alternative Lagrange Euler (ALE)
  Level set or phase field.
  Shallow water eqns.
Multiple fluids
  Two fluids with interface
  Level set or phase field to track interface, surface tension, adhesion
Porous media
  Fluid saturation varies
  Richard’s equation, variable water saturation
  Two-three phase Darcy, two or more fluids.

## Slide 5: Outline
Review approach for single phase fluid
Variations
  Two fluids
  Mixtures
  Free surface
  Porous media

## Slide 6
Conservation of Mass
c = r
Storage
Advective Flux
No Diffusive Flux
Source
Governing
A= uc =ur

## Slide 7
Conservation of Momentum
c = ru
A= uc= uur
Storage
Advective Flux
Diffusive Flux
Source
Governing
Units of stress or pressure

## Slide 8: Constitutive Equation (stress to strain rate)
Navier-Stokes for Incompressible Fluid
Momentum Equation Rearranged
( Comsol notation)

## Slide 9: Boundary Conditions
Specify pressure
Specify velocity
n unit vector normal to boundary
u flux vector
C1 known function
Inlet, Outlet, Wall, Open, other
No slip, wall = default
Specify inlet and outlet
Need to specify pressure somewhere

## Slide 10: Options for boundary conditions
Velocity (uniform) =0.001m/s
Laminar Inflow = 0.001 m/s
1m entrance length
Pressure = 1
No viscous stress
Pressure=0
No viscous stress
Pressure=0
No viscous stress
Pressure=0
No viscous stress
Need to calculate Pressure in top two cases, calculate velocity in bottom case

## Slide 11: Discrete Fluid Phases Small scale
http://oc.wikipedia.org/wiki/Fichi%C3%A8r:Oil_in_water.jpg
http://www.flickr.com/photos/fdecomite/2141150298/lightbox/
Drops of oil in water
Surface tension
Oil and water at pore scale
Surface forces solid-oil-water
 Boundaries between fluid phases

## Slide 12
1
2
s

## Slide 13: Oil in water Macro-mega scale
http://www.eoearth.org/article/Deepwater_Horizon_oil_spill?topic=50364
http://corollaries.unc.edu/tag/camassa/
http://www.backyardxscapes.com/blog/gulf-of-mexico-affecting-indigenous-wildlife-and-perhaps-much-more/
Bands of oil floating in the ocean

## Slide 14: Algae

## Slide 15
Two Fluids with Contrasting Density
http://pof.aip.org/gallery_of_fluid_motion
[Sayag eta l. 2012]

## Slide 16: Instability with two fluids
http://fluidlab.arizona.edu/RT_Incomp.html
Low visc displaces high visc fluid in Hele Shaw cell
http://www.sciencedirect.com/science/article/pii/S0894177709000144
High density over low density fluid
High g experiment
min/mambient decreases

## Slide 17: Large-scale Instability Salt Dome in Sediments
http://wholefish.blogspot.com/2009/05/salt-rulescooking-and-fishing.html
http://www.gocad.org/w4/index.php/research/gallery
http://blogs.agu.org/georneys/files/2011/07/Brazil-Margin-Salt_edited.jpg
http://homepage.ufp.pt/biblioteca/GlossarySaltTectonics/Pages/PageD.html

## Slide 18: Analyzing Two separate fluids
Mass and momentum for each phase
Track the interface between phases
Use continuous variable with rapidly changing (but not sharp) transition.
Level set, Phase field
Level Set Function defining phases

## Slide 19: Level Set Method
Mass Conservation
Momentum
Level Set Parameter, f
Unit vector normal to interface

## Slide 20: Applications of Level Set Method
Nozzle droplet, rising bubble .gif

## Slide 21: Moving Mesh
Moving mesh vid

## Slide 22: Mixtures of fluids and particles Particles in gas
Saltation of sand on a dune
Pyroclastic flow
Mt. St Helens, 7 Aug. 1980
http://en.wikipedia.org/wiki/File:Pyroclastic_flows_at_Mayon_Volcano.jpg
http://geology.com/volcanoes/volcanic-hazards/
Smoke plume from fire at oil refinery
Air emission from industry
http://www.sfexaminer.com/local/2012/08/fire-breaks-out-chevron-refinery-richmond
Fluidized bed reactor
http://www.flickr.com/photos/rossdu/1357737030/

## Slide 23: Solid particles in fluid
http://homepages.engineering.auckland.ac.nz/~hfri003/projects.htm
http://serc.carleton.edu/images/NAGTWorkshops/sedimentary/activities/flume4.jpg
http://discoverytimes.blogspot.com/2008/11/black-smoker-discovered-along-with-500.html
http://www.flickr.com/photos/rossdu/1357737030/lightbox/
Hydrothermal vent
Sediment plume from Moore Creek entering Dog River after heavy rain.
http://www.usouthal.edu/geography/fearn/480page/98Gerrit/SedPlume.html
Turbidity current in lab flume
http://www.whoi.edu/redtide/
Noctiluca scintillans in New Zealand. (Photo by M. Godfrey)
Phytoplankton

## Slide 24: Gas-liquid mixtures
http://biologyblockb.blogspot.com/2010/12/aerosol-spray-by-sammy-bozza.html
http://footage.shutterstock.com/clip-826795-stock-footage-beer-bubbles-background.html
http://my.opera.com/cofoppyplop/albums/showpic.dml?album=371184&picture=5315272
Fly Geyser, NV
Achoo
Fluid droplets in gas
Gas bubbles in fluid

## Slide 25: Particles in fluid
Euler-Euler method and related
  1 continuous fluid, 1 dispersed phase
  Vol fraction, f, controls visc/density
  Transfer between particles and fluid
  Momentum
  Mass
  Heat
  Particle hydrodynamics
  Shape, size, coalescence, dispersion, breakup, collisions with wall/other particles….

## Slide 26
Conservation of Mass
Continuous phase, c, and dispersed phase, d
cc = rcfc
cd = rdfd
Storage
Advective Flux
Source
Governing
rc = density
fc = vol fraction
Sc=Mc
Sd=Md
Couple to get 1

## Slide 27
Conservation of Momentum
Approachanalyze mixture
Storage
Advective Flux
Diffusive Flux
Source
= density of mixture
c = ru
Governing

## Slide 28: Key aspects
Couple momentum cd
Slip velocity
Properties of mixture
Volume fraction solids in fluidized bed reactor

## Slide 29: Alternative Approach: Particle Tracking
Follow explicit particles in the flow.
Fluid parcels in continuous fluid
Particles with mass, drag, etc.
Many particles possible
Rotating mixer

## Slide 30: Example Flow regimes during two phase flow in a vertical microtube
http://www.sciencedirect.com/science/article/pii/S0301932207001772

## Slide 31
http://www.sciencedirect.com/science/article/pii/S0043164805001882
http://www.sciencedirect.com/science/article/pii/S095559861000004X
Gas-oil mixture images with high-resolution wire mesh sensor
Conceptual Model for Gas-Liquid Flow in a Vertical Pipe.
http://dpwsd.waterworld.com/index/display/article-display/3887904678/articles/membranes/volume-2/issue-30/Features/Importance_of_Air_Scour_in_Membrane_Bioreactor_Systems.html

## Slide 32: Free-surface flow
http://upload.wikimedia.org/wikipedia/commons/4/43/2006-01-14_Surface_waves.jpg
http://en.wikipedia.org/wiki/File:Fjord.surface.wave.boat.jpeg
http://flyadvisor.blogspot.com/2011/08/legendary-big-wave-surfing.html
http://news.nationalgeographic.com/news/2012/03/pictures/120309-japan-tsunami-earthquake-anniversary-fukushima/
Ripples from a water drop
Wake behind a boat, drag resistance
Sloshing in a tank
Flow over seawall during tsunami
Flow over seawall during Katrina storm surge
Displacement of water table
http://news.monstersandcritics.com/usa/features/article_1573085.php/In-Pictures-USA-Iowa-Dam-Break
Dam failure on Maquoketa River, Iowa

## Slide 33: Free surface
Level set
  Second fluid is air
Moving Mesh
  Move upper boundary with fluid
  Arbitrary Lagrangian Eulerian (ALE) method
Shallow water eqns
  Average NS over depth
  Solve directly for depth

## Slide 34: ALE Method Moving Mesh
Use boundary condition so boundary moves with fluid
e.g. Velocity of boundary = u*nx+v*ny
Boundary moves, entire mesh readjusts.
Problems with large displacements, distorted mesh
Possible to pause, regenerate mesh, restart analysis
Pull plug, tsunami.gif

## Slide 35: Shallow water equations
Shallow water
t = 0
c=hr
M/A
c=hru
Mv/A

## Slide 36: Examples
Video : surface water waves

## Slide 37: Porous media
http://acswebcontent.acs.org/prfar/2009/G8.html
https://www.agronomy.org/publications/sssaj/articles/66/2/347
Infiltration of dyed water into Hanford sandy loam, even wetting front
Variable saturation with water
Multiple fluids, pore to field scale
NAPL-water-gas-supercritical
http://www.sciencedirect.com/science/article/pii/S0920410500000905
Infiltration of dyed water into sand. Preferential flow
Infiltration tracer test
NAPL in lab experiment

## Slide 38
Conservation of Mass
c = rfSe
Storage
Advective Flux
No Diffusive Flux
Source
Governing

## Slide 39
Conservation of Momentum
c = rv
A= vc= vvr
Storage
Advective Flux
Diffusive Flux
Source
Governing
Units of stress or pressure

## Slide 40: Flow in Porous Media
Mass
Momentum
Constitutive