## Slide 1: Flow Through Porous Media
Applications and examples
Conceptual model
Analysis
  Governing equations
  boundary/initial conditions,
  parameters
  Scaling, dimensionless numbers
Exercise
Historic picture of Thousand Springs, Idaho

## Slide 2
http://www.thermaxindia.com/Water-and-Waste-Solutions/Systems-and-Solutions/Filtration.aspx
http://www.dgssupply.dk/dgs-info/irrigation.html
http://www.poolcenter.com/filter_poolstor_pentair.htm
http://sti.srs.gov/fulltext/ms2002431/ms2002431.html
Sintered nickel filter media
Home water filter
Sand filter for a swimming pool
Industrial filter
Sand Filter
Trap material in water

## Slide 3
http://www.ameriwater.com/products/industrial/cooling-tower-filtration/
High Efficiency Sand Filter
Trap material in water, reduce clogging

## Slide 4
Darcy’s Experiment
Design Water Filter

## Slide 5
Plants
Nutrients, heat, growth
Cross-section of a monocot root, showing cortex, pith and vascular tissue. Image courtesy of Wendy Paul
http://sci.waikato.ac.nz/farm/content/plantstructure.html
Section through woody tissue, showing xylem tracheids. Image courtesy of Roberta Farrell.
http://serc.carleton.edu/eslabs/weather/1d.html
http://ugt-online.de/en/produkte/oekologie/saftfluss-und-wasserpotenzial/xylemflusssensor-hfd.html
Water flow from soil to atmosphere through a tree

## Slide 6: Two-way porous media flow in plants
Sap flow meter
Water with inorganic nutrients flows from roots to leaves through xylem, sugar produced in leaves flows down the phloem.
http://kids.britannica.com/elementary/art-66141/Cross-section-of-a-tree-trunk
[Kent, 2000]

## Slide 7: Porous media flow in mammals Many essential processes in biology
Lung tissue
Aveola pore in lung
Cross-section of aveola. Blood capillaries in dark grey
http://www.sciencedirect.com/science/article/pii/S109564330000218X
http://www.nature.com/pr/journal/v55/n2/fig_tab/pr200444f8.html
Cast of arterial blood vessels in the kidney
http://www.scielo.cl/scielo.php?script=sci_arttext&pid=S0717-95022009000300024&lng=en&nrm=iso&ignore=.html
Pores in kidney tissue

## Slide 8: Rock and sediment Recovery of important resources
Original void space
Photomicrograph of Nubian sandstone
Photomicrograph of carbonate rock,
blue is pore space
Christopher Kendall, 8/17/2005 ,http://strata.geol.sc.edu kendall@sc.edu
Vesicular basalt, Hawaii meteorites.wustl.edu/id/vesicles.htm
Beach sand, Rodeo Beach, CA
http://www.msnucleus.org/membership/html/k-6/rc/rocks/3/images/rckr06.jpg

## Slide 9: Pore space in Sandstone From x-ray tomography
22 percent porosity 7 percent porosity
1 mm

## Slide 10: 3-D Pore space with computed tomography
http://www.netl.doe.gov/newsroom/labnotes/2010/11-2010.html
Sandstone
Connected pores: white
Disconnected pores: red
Image size: 1.2 mm
Shale
Connected pores: red
Disconnected pores: green
Main flow path: blue

## Slide 11
micron
Shale SEM CT

## Slide 12
Aquifers and confining units
Notes: Rainfall cycle
Aquifer types

## Slide 13: Oil and Gas Reservoirs
Interbedded gravel, coarse- and fine-grained sand stone
http://www.southampton.ac.uk/~imw/Oil-South-of-England.htm
Spindletop well, TX
http://www.sjvgeology.org/history/lakeview/spindletop_bg.jpg

## Slide 14
Analyze fluid flow
through porous media
Objective: Determine flux and pressure
Conceptual model
Governing Equations
Boundary Conditions
Properties
Examples

## Slide 15: General Concepts
Average properties over REV, REV>>pores
  continuum
Mass of fluid is conserved
Momentum is conserved

## Slide 16: Continuum Representative Elementary Volume
Average the effects of complex pore geometries
REV

## Slide 17: Average Properties over REV
1
0
REV Size
Porosity
Use volume average of properties

## Slide 18: Governing Eqns
Problem: Flux and pressure are unknowns. They are what we want to determine.
Approach: Two unknowns, need two governing equations
  Conservation of momentum
  Conservation of mass
Implementation:
1. general expressions first, then tailor them for porous media
2. Start here:
Divergence of flux vector plus rate of storage change equals the rate of source production

## Slide 19
Conservation of Mass
c = rfSe
Storage
Advective Flux
No Diffusive Flux
Source
Governing
r: fluid density
F: porosity
Se : degree of saturation

## Slide 20
Conservation of Momentum
c = rv
A= vc= vvr
Storage
Advective Flux
Diffusive Flux
Source
Governing
Units of stress or pressure
Use pore only as CV

## Slide 21
Slow (laminar) flow with no acceleration or body forces
Gauss’s Theorem
average

## Slide 22
Hagen-Pouiselle Law for laminar flow in tube
Force balance
Substitute into HP
Sub into average

## Slide 23
Darcy’s Law is conservation of momentum averaged over the REV
Need to include gravity for vertical flow
Darcy’s Law for horizontal flow
Body force in fluid
Need to start from two slides ago and revise. The result is
In terms of hydraulic head

## Slide 24: Things you need to know to define a process
Governing equations
Conservation Laws, constitutive equations
Define dependant variable(s)
Possibly multiple, coupled
Boundary conditions
Dirichlet, Neumann, Cauchy-type, other;
names vary with process
Properties
Constant
Spatially variable (heterogeneous)
Temporally variable, controlled externally
Temporally variable, coupled to dependent variable
Sources
Constant
Spatially variable (heterogeneous)
Temporally variable, controlled externally
Temporally variable, coupled to dependent variable

## Slide 25: Implementation Hydraulic head as dependent variable
Governing Equations
  Mass balance
  Momentum balance—flow law
  Dependent variable
    Hydraulic head, h = p/g + z [L]
Properties
r: fluid density [M/L3]
Ss: specific storage [1/L]
k: permeability [L2]
g: gravity acceleration [L/T2]
m: viscosity [M/LT]
Source
Qm: mass source [M/(L3T)]
z: upward coordinate [L]
u: volumetric flux vector [L/T]

## Slide 26: Defining Flow through Porous Media Pressure as dependent variable
Governing Equations
  Mass balance
  Momentum balance—flow law
  Dependent variable
    pressure, p [M/LT2]
Properties
r: fluid density [M/L3]
Ss: specific storage [1/L]
k: permeability [L2]
g: gravity acceleration [L/T2]
m: viscosity [M/LT]
Source
Qm: mass source [M/(L3T)]
D: upward coordinate [L]
u: volumetric flux vector [L/T]

## Slide 27: Boundary Conditions All external boundaries
Dirichlet (specified head/pressure)
Neumann (specified gradient or flux)
Cauchy (head dependent flux)
h=C1
n
n.u
n unit vector normal to boundary
u flux vector
C1 known function

## Slide 28: Initial Conditions
Transient problems
Must specify values of c (head or pressure) at t=0.
Base on info about the problem, conditions at the start
i.c. not needed for steady state.
One strategy is to run a steady state problem and use the results as initial conditions for transient problem

## Slide 29: Properties
Properties
r: fluid density [M/L3]
k: permeability [L2]
g: gravity acceleration [L/T2]
m: viscosity [M/LT]
cs: compressibility [1/P]
Needed for transient models only
Hydraulic conductivity
Assume properties are constant for basic problems (saturated, locally deformable).
Properties vary as functions of h or p if unsaturated, non-local deformation

## Slide 30
http://www.engineeringtoolbox.com/liquids-densities-d_743.html
Fluid Properties
Depend on P, T, C, other. Values for standard conditions

## Slide 31: Porous media properties

## Slide 32: Units
Default is SI: m, kg, s, Pa
Write with square brackets: 23[m] 12[Pa]
Can change units system
Using units helpful, but not required. Orange color on equation indicates problem with units.
Recommend using SI
Water density: 1000 [kg/m^3]; viscosity: 0.001 [kg/(m*s)]; g: 981 [m/s^2]

## Slide 33: Examples
Steady flow between two streams
Transient flow between two streams
Transient flow to a well
Transient flow in a tree

## Slide 34: Example, flow between two streams
What is the hydraulic head and flow between two streams?
K=1E-6 m/s; recharge R=1E-9 m/s; thickness b=10m. Qm = R*density/b
Stream
CH boundary
1000 m

## Slide 35: Boundary conditions
x
h1 h2
b
Conceptual model
b.c. 1: h = h1 @ x = 0
L
b.c. 2: h = h2 @ x = L

## Slide 36: Use b.c. to solve for constants
b.c. 1: h = h1 @ x = 0
b.c. 2: h = h2 @ x = L

## Slide 37: Substitute constants and solve for h
Assume L=1000m, b=25m

## Slide 38: Exercise, steady state
1. Determine heads using specified geometry and parameters
  Plot heads as color flood, contours
  Plot flow vectors, streamlines
2.Include head gradient in stream using h=y*0.02 on boundary. Repeat above

## Slide 39: Exercise, Transient
h=1
1000 m
h=0
Include “Storage Model,” Same properties as above. “user defined” Storage Model, S=1E-8 1/Pa
Assume h=0 as initial conditions (default)
h=1 at boundary. This will cause pressure wave to propagate from left to right.
Run transient 0<t<3E7s.
Plot head along cross section normal to boundaries

## Slide 40: Verify transient problem

## Slide 41: Steady State as Initial Conditions
The previous transient example assumed initial conditions were uniform, h=0. What if the initial conditions were actually the steady state conditions?
Add new study, stationary. Set up conditions for stationary model, solve.
Then change b.c. (raise the head along boundary). Change transient study solver configuration dependent variables initial values of variables solved forselect the stationary solution. See following screen capture.

## Slide 42: Transient pumping test
In the field: pump well at constant rate, measure pressure as function of time.
Simulation: pump well at constant rate, simulate pressure, adjust parameters until simulations match field data.

## Slide 43: Example
Pumping rate 7 cfm,
Radial distance to monitoring well, r = 50 ft,
Aquifer thickness, b = 25 ft
Distance to stream L=150 ft
Assume rwell = 0.25 ft
Drawdown at well = 90 ft at t=1000 minutes.
Determine T, K, and S
Well efficiency, Specific capacity
T = 0.13 ft2/s
S = 0.001
Well efficiency: 0.73
150ft
data

## Slide 44: Flow in a tree