## Slide 1: Project
Concept
Proposal
Status Reports
Final report
Presentation

## Slide 2: Advection and Dispersion
Fresh ash plume from Eyjafjallajokull volcano
http://blogs.crikey.com.au/planetalking/2011/02/02/nature-v-air-travellers-and-everyone/

## Slide 3
Plumes, jets, and mixing
http://therapidian.org/water-quality-grand-river
http://www.globalunderwaterexplorers.org/content/ames-sink-tracer-test
http://therapidian.org/water-quality-grand-river
http://www.newswise.com/articles/good-vibrations-from-deep-sea-smokers-may-keep-fish-out-of-hot-water
Jet of birefringent fluid
A free jet issuing into a quiescent fluid. The flow rate of the jet is around 2 cm/ sec; the volume of the jet is around 50 mL. The horizontal length of the field of view is about 15 cm. The flow visualization uses an inorganic, streaming birefringent fluid
http://www.efluids.com/efluids/gallery/gallery_pages/Blackstock.jsp
Grand River into Lake Michigan
Dye Tracer in Stream
Hydrothermal vent
Groundwater plume, Paducah, KY

## Slide 4
http://www.crustbuster.com/Products/dry-fertilizer-products~blending-and-handling.html
http://water.me.vccs.edu/math/flocculation_math.html
http://en.wikipedia.org/wiki/File:Chemineer_Kenics_Static_Mixer.JPG
Clemson Waste Water Treatment Plant
Static Mixers
Mix fluids using energy from flow alone
In-line Mixer
Chlorine Mixing Tank

## Slide 5: Active Mixers
http://www.crustbuster.com/Products/dry-fertilizer-products~blending-and-handling.html
http://water.me.vccs.edu/math/flocculation_math.html
http://en.wikipedia.org/wiki/File:Chemineer_Kenics_Static_Mixer.JPG

## Slide 6: Advection and Diffusion
Advection: Transport of substance due to bulk motion of fluid. a.k.a convection (heat)
Advective mass flux: uC
Diffusion:
Source w/ disp
advection

## Slide 7: Dispersion
Types: Longitudinal, Transverse
Causes
  Gradient in flow velocity
    Laminar , Taylor dispersion
    Turbulent
  Splitting of flow paths
    Turbulent
    Mechanical

## Slide 8: Gradient in flow velocity
Longitudinal dispersion from velocity gradients
Molecular diffusion (green) reduces longitudinal dispersion

## Slide 9: Splitting of flow paths
Mechanical
Turbulent
Transverse Dispersion
Longitudinal Dispersion
Transverse Dispersion
Longitudinal Dispersion

## Slide 10: Mechanical Dispersion
Photomicrograph of pore space
Constant head and no flow boundaries
Color is head, lines are streamlines
Source of contaminant
Movement of mass due to splitting of flow paths, fluctuations in velocity, other. Demo

## Slide 11: Dispersive Flux
Porous media
Turbulent flow

## Slide 12
Storage
Advective Flux
Diffusive Flux (Fick’s Law)
Dispersive Flux
Source
Governing
Conservation of Mass
Advection-Dispersion
c = C
S=0 (for now)

## Slide 13: Simulation of Advection-Dispersion
Governing
Boundary
Dirichlet, Specify Conc
Neuman, Specify diffusive flux
Specify advective flux
Cauchy, flux proportional to gradient
Need to know q
Constant, q
One-way coupling
    q(t)C
Two-way coupling
  q(t)C

## Slide 14: Mechanical Dispersion in Porous Media
aL: longitudinal dispersivity[L]
aT: transverse dispersivity[L]
Other formulations available

## Slide 15: Plume in 1D flow

## Slide 16: Example 1D flow

## Slide 17: Dimensionless Form

## Slide 18: Peclet Number
L: characteristic length
vx: velocity
D: diffusion or dispersion
tflow = L/v
tdiffuse = L2/D
Relative importance of advection and diffusion
Important time scales
Peclet Number

## Slide 19: Dispersion and Peclet
http://www.sciencedirect.com/science/article/pii/S0169772211000180

## Slide 20: Numerical Stability and Peclet
Cell Peclet number
Cell Peclet> 10-100 will cause problems
Decrease h or increase D
Particle tracking

## Slide 21
Dispersion at different Peclet Numbers
http://download.springer.com/static/pdf/613/art%253A10.1007%252Fs11270-006-9296-6.pdf?auth66=1363234017_ff68087b7f7be6bc5abd393dcab29e81&ext=.pdf
Theodoropoulou et al. 2003

## Slide 22: Dispersion in channels, conduits... Gradient in flow velocity
Longitudinal dispersion + diffusion in laminar flow
Longitudinal and transverse dispersion in turbulent flow

## Slide 23: Turbulent Flow

## Slide 24: Turbulent Dispersion
Vortices occur over all scales, but the largest ones give the largest Dm
Need to be the largest vortices not explicitly simulated.

## Slide 25: Estimating Dm
Laminar flow, pipe:
Turbulent pipe: D = 10.1 R ush; ush=(to/rw)1/2
Porous media: D = D*+aLu
Infinitely wide channel: D=5.93 d ush
Vertical mixing in stream: D=0.067 d ush
Longitudinal in stream:

## Slide 26: Values for Dm (m2/s)
Rivers
Vertical 10-1-1
Transverse 10-1-1
Longitudinal 10-1-103
Lakes
vertical 10-5-10-2
Transverse 10-3-1
Ocean 10-3-104

## Slide 29: Grand River Plume

## Slide 31: Peclet Number
L: characteristic length
vx: velocity
D: diffusion or dispersion
d: diameter of source
W: width of plume
DL: travel distance
Peclet Number
DL
W

## Slide 32: Dispersion in Porous Media
Photomicrograph of pore space
Constant head and no flow boundaries
Color is head, lines are streamlines
Longitudinal Dispersivity (m)
1000
100
10
1
0.1
0.01
1 10 100 1000 10,000 100,000
Scale of measurement (m)
aL=0.1x